## Slide 1
Training Review
CMOS DESIGN

## Slide 2: Contents
CMOS – Structure and operation
Others CMOS design
CMOS Memory
Inverter – the Not logic gate
Width/Length – Voltage - Temperature

## Slide 3: CMOS Structure and Operation
S
G
D
B
G
D
B
S
p type wafer
n-well
n+
n+
n+
p+
p+
p+
PMOS
NMOS
S
B
G
D
D
G
S
B
NMOS
PMOS

## Slide 4: CMOS Structure and Operation
G
G
D
S
B
p substrate
n+
n+
p+
NMOS
G
Cross section of an MNOS transistor
Thin Oxide (SiO2)
Poly (Gate)
Length (L)
Width (W)
W/2
NMOS structure

## Slide 5: CMOS Structure and Operation
NMOS operation depend on Gate voltage
1. Accumulation
2. Depletion
3. Inversion
Accumulation
Depletion
Inversion
Increase VG
VT

## Slide 6: CMOS Structure and Operation
NMOS operation modes
1. Cutoff : VGS < VT
2. Nonsaturation : VGS ≥ VT and VDS ≤ (VGS – VT)
3. Saturation : VGS ≥ VT and VDS ≥ (VGS – VT)

## Slide 7: CMOS Structure and Operation
NMOS operation modes
n+
n+
p- subtrate
Vb=0
Depletion
electron layer
VS=0
0<VT0<VgS
VD=0
+ + + + + + + + + + + + + + + + + +
VS=0
0<VgS<VT0
VD=0
n+
n+
p- subtrate
Vb=0
Depletion
+ + + + + + + + + + + + + + + + + + + + +
VS=0
VDS<(VgS-VT0)
0<VT0<VgS
n+
n+
p- subtrate
Vb=0
Depletion
+ + + + + + + + + + + + + + + + + +
VS=0
0<VT0<VgS
L-L
L
VDS>(VgS-VT0)
+ + + + + + + + + + + + + + + + + +
ID
VDS
Linear
Non-Linear
Saturation
VDS
ID
In linear mode, MOS acts like a resistor varying linear with VGS

## Slide 8: CMOS Structure and Operation
NMOS – V threshole
Vb=0 VT = VT0
VT0 phu thuoc the Fermi, nong do doping Na, hang so dien moi Si, Dien dung gate / chieu dai gate Cox
Delta VT tang khi tang VB.

## Slide 9: CMOS Structure and Operation
Overlap Capacitors in Mosfet
Cols = CoxWLs
Cold = CoxWLd

## Slide 10: CMOS Structure and Operation
1. Cutoff: no inversion layer channel
Gate Capacitors in Mosfet
2. Nonsaturation:
3. Saturation:

## Slide 11: CMOS Structure and Operation
VgS>0
VDS>0
VgS<0
VDS<0
ID
ID
NMOS vs PMOS

## Slide 12: CMOS Structure and Operation
Depletion n-channel Mosfet

## Slide 13: Inverter – the Not logic gate
Ideal Inverter
Voltage transfer Characteristic (VTC)
Transient response

## Slide 14: Inverter – the Not logic gate

## Slide 15: Inverter – the Not logic gate
NMOS Inverter structure
The load device can be:
Linear Resistor
Saturated n-Mos
Depletion n-Mos
Non-saturated n-Mos

## Slide 16: Inverter – the Not logic gate
Inverter with Linear Resistor Load
Power dissipate when nMos on

## Slide 17: Inverter – the Not logic gate
Vin
Vin
Rn
Rp
vdd
in
out
0v
S
G
D
B
G
D
B
S
NMOS
PMOS
Vout
0.5vdd
R
vdd
CMOS Inverter

## Slide 18: Inverter – the Not logic gate

## Slide 19: Inverter – the Not logic gate

## Slide 20: Inverter – the Not logic gate
Why use CMOS
Disdvandtages
+ Processing is more complex than NMOS
+ Additional processing for latch-up prevention
+ CMOS require more transistors than equivalent NMOS-designs
Advandtages
+ CMOS circuits dissipate power only during switching events
+ VOH = VDD and VOL = 0V
+ VTC of a CMOS inverter will exhibit a sharp transition

## Slide 21: Latch-up in CMOS
p-substrate
p+
n+
n+
n-well
p+
p+
n+
GND
Vdd
In
Out
Vdd
GND
Out
0
Noise
Vdd
p+
p+
n
p
n+
n+
n+
p+
GND
Out
Rwell
Rsub
Q1
Q2
Q1
Q2
Rwell
Rsub
Q2
Q1

## Slide 22: Latch-up in CMOS
Latch-up Effect

## Slide 23: Others CMOS design
a CMOS
circuit
G
D
B
S
S
G
D
B
S
G
D
B
VDD
A
Y
VSS
G
D
B
S
P1
N0
N1
P0
CKB
CK
VDD
A
Y
VSS
Rp0
CKB
CK
Rp1
Rn1
Rn0
VDD
VSS
Y
A
INVZ
CK
CKB
Symbol
If [(CK=1)&(CKB=0)]
This becomes INV
If not [(CK=1)&(CKB=0)]
Output is isolated from input, this is called high Z state
CMOS InverterZ

## Slide 24: Others CMOS design
a CMOS
circuit
S
P0
VDD
D
B
G
N0
G
D
S
B
VSS
CKB
CK
IN
OUT
0v
CL
IN
OUT
Rp
Rn
CKB
CK
0: close
1: close
H
+
0v
CL
IN
OUT
Rp
Rn
CKB
CK
0: close
1: close
L
+
0
vdd
Vin
Rp
Rn
Req
CMOS TGate

## Slide 25: Others CMOS design
CMOS TGate

## Slide 26: Others CMOS design
Latch Circuit
CKB
OUT
IN
TGATE
CK
VDD
VSS
VDD
VSS
Y
A
INV
VSS
VDD
Y
A
INV
CK
CKB
Din
Dout
a
CKB
OUT
IN
TGATE
CK
VDD
VSS
b
Din
CK
CKB
a
Dout
b
Latch
a = Din
Latch
a = Din

## Slide 27
CKB
OUT
IN
TGATE
CK
VDD
VSS
VDD
VSS
Y
A
INV
VSS
VDD
Y
A
INV
CK
CKB
Din
Dout1
a1
CKB
OUT
IN
TGATE
CK
VDD
VSS
b1
CKB
OUT
IN
TGATE
CK
VDD
VSS
VDD
VSS
Y
A
INV
VSS
VDD
Y
A
INV
Dout2
a2
CKB
OUT
IN
TGATE
CK
VDD
VSS
b2
Din
CK
CKB
a1
Dout1
a2
Dout2
Latch
Latch
Latch
Latch
CMOS DFF using TGATE

## Slide 28
CK
Din
Dout1
a1
b1
INV
Dout2
a2
b2
Gate1
Gate2
Gate3
Gate4
Gate1,4
Gate2,3
ON
ON
OFF
ON
OFF
OFF
Din  Dout1
Dout1  Dout2
Latch Dout2
Din  Dout1
Latch Dout2
Feed through may occur during this time
CK
0
1
0
CMOS DFF using TGATE

## Slide 29
CK
Din
Dout1
a1
b1
INV
Dout2
a2
b2
Gate1
Gate2
Gate3
Gate4
Insert buffer to prevent feed through
Create internal clock
Master stage
Slave stage
Delay
Output buffer
An example of DFF circuit
CMOS DFF using TGATE

## Slide 30: Others CMOS design
Latch - InverterZ

## Slide 31: Others CMOS design
Latch - InverterZ

## Slide 32: Others CMOS design
DFF InverterZ

## Slide 33: Others CMOS design
DFF InverterZ

## Slide 34
CMOS NAND gate
A
Y
VDD
VSS
S
G
D
B
G
D
B
S
G
D
B
S
S
G
D
B
B
N0
N1
P0
P1
Y
A
B
NAND
VDD
VSS
VDD
A
Y
VSS
B
1
1
0
Y = A.B
Y = 0 only one case: A = 1 and B = 1

## Slide 35
B
Y
VDD
VSS
S
G
D
B
G
D
B
S
S
G
D
B
A
N0
N1
P1
P0
G
D
B
S
VDD
VSS
A
B
Y
NOR
VDD
B
Y
VSS
A
CMOS NOR gate
0
0
1
Y = A+B
Y = 0 if there is any input = 1

## Slide 36: Width/Length – Voltage - Temperature
Width/Length – Voltage - Temperature
Design parameter
Width/Length
Wn = 0.2um
Wn = 0.1um

## Slide 37: Width/Length – Voltage - Temperature
vdd
in
out
0v
S
G
D
B
G
D
B
S
NMOS
PMOS
CL
PMOS
NMOS
time
Vin
Vout
ON
ON
OFF
OFF
ON
ON
vdd
0v
0.5vdd
Depends on Cin_out and input slew
Longer t, higher power consumption
weaker NMOS
stronger NMOS

## Slide 38: Width/Length – Voltage - Temperature
vdd
in
out
0v
S
G
D
B
G
D
B
S
NMOS
PMOS
CL
Depends on Cin_out and input slew
PMOS
NMOS
time
Vin
Vout
ON
ON
OFF
vdd
0v
0.5vdd
ON
ON
OFF
weaker PMOS
stronger PMOS
Longer t, higher power consumption

## Slide 39: Width/Length – Voltage - Temperature
Vin
Vin
Rn
Rp
Vout
vdd
0.5vdd
R
vdd
in
out
0v
S
G
D
B
G
D
B
S
NMOS
PMOS
stronger NMOS
weaker PMOS

## Slide 40: Width/Length – Voltage - Temperature
Vin
Vin
Rn
Rp
Vout
vdd
0.5vdd
R
vdd
in
out
0v
S
G
D
B
G
D
B
S
NMOS
PMOS
weaker NMOS
stronger PMOS

## Slide 41: Width/Length – Voltage - Temperature
Vin
Vin
Rn
Rp
Vout
vdd
0.5vdd
R
vdd
in
out
0v
S
G
D
B
G
D
B
S
NMOS
PMOS
What would a designer expect?
A designer would expect Vout = 50% of vdd when Vin = 50% of vdd

## Slide 42: Width/Length – Voltage - Temperature
Wn = Wp
Wn = 9Wp
 | tpLH | tpHL
Wp = Wn | 4.351ps | 1.932ps
Wp = 2Wn | 4.012ps | 2.574ps
Wp = 3Wn | 3.674ps | 3.402ps
Wp = 4Wn | 3.395ps | 4.443ps
Effect with Inverter :

## Slide 43: Width/Length – Voltage - Temperature
Temperature
Green line : 25 0C
Yellow line : 120 0C
 | tLH | tHL | AVG Power
-40 oC | 10.84ps | 12.38ps | 117.4 nW
25 oC | 12.08ps | 12.71ps | 191.5 nW
120 oC | 13.46ps | 13.52ps | 448.0 nW_-
Effect with Inverter :

## Slide 44: Width/Length – Voltage - Temperature
Sweep Temperature, use Transient simulation, measure time delay
tLH tHL tpLH tpHL
Temp = -4 1.157e-11 1.256e-11 4.408e-12 2.653e-12
Temp = 6 1.175e-11 1.261e-11 4.272e-12 2.616e-12
Temp = 16 1.197e-11 1.267e-11 4.102e-12 2.589e-12
Temp = 26 1.210e-11 1.272e-11 4.001e-12 2.572e-12
Temp = 36 1.225e-11 1.280e-11 3.886e-12 2.556e-12
Temp = 46 1.240e-11 1.287e-11 3.783e-12 2.547e-12
Temp = 56 1.264e-11 1.294e-11 3.690e-12 2.544e-12
Temp = 66 1.269e-11 1.302e-11 3.598e-12 2.543e-12
Temp = 76 1.288e-11 1.310e-11 3.512e-12 2.545e-12
Temp = 86 1.296e-11 1.320e-11 3.438e-12 2.548e-12
Temp = 96 1.308e-11 1.329e-11 3.366e-12 2.553e-12
Temp = 106 1.328e-11 1.339e-11 3.304e-12 2.561e-12

## Slide 45: Width/Length – Voltage - Temperature
Sweep Wn, use Transient simulation, measure time delay
tLH tHL tpLH tpHL
Wn = 0.1 1.063e-11 1.084e-11 4.163e-12 2.810e-12
Wn = 0.2 1.041e-11 1.043e-11 4.639e-12 2.520e-12
Wn = 0.3 1.042e-11 1.010e-11 5.272e-12 2.007e-12
Sweep Vin, use Transient simulation, measure time delay, AVG Power
tHL tLH tpHL tpLH
Vsup = 0.9Vdd 1.160e-11 1.175e-11 4.340e-12 2.768e-12
Vsup = 0.95Vdd 1.116e-11 1.126e-11 4.258e-12 2.799e-12
Vsup = 1Vdd 1.063e-11 1.084e-11 4.163e-12 2.810e-12
Vsup = 1.05Vdd 1.028e-11 1.046e-11 4.087e-12 2.820e-12
Vsup = 1.1Vdd 9.908e-12 1.008e-11 4.014e-12 2.834e-12
Vsup = 1.15Vdd 9.572e-12 9.822e-12 3.943e-12 2.839e-12

## Slide 46: Width/Length – Voltage - Temperature
Fanout Effect
 | deLH | deHL
Driver 1 Inver | 7.593ps | 7.857ps
Driver 2 Invers | 10.37ps | 10.58ps

## Slide 47: CMOS Memory

## Slide 48
Part 1
Read Only Memory
ROM
Notes: 48
Slide covers the agenda of what’s to follow.

## Slide 49
One column
ROM cell array
Example: 4x4 cell array
0
0
0
1
0
1
0
0
0
1
1
0
1
0
0
1
VDD
VDD
VDD
VDD
W3
W2
W1
W0
BL3
BL2
BL1
BL0
Missing contact: Bit 0
Existing contact: Bit 1
One row
Notes: 49
Slide covers the agenda of what’s to follow.

## Slide 50
Rp
Rp
Rp
Rp
50
0
0
0
1
0
1
0
0
0
1
1
0
1
0
0
1
VDD
VDD
VDD
VDD
W3
W2
W1
W0
BL3
BL2
BL1
BL0
ROM cell array
Example: 4x4 cell array
Notes: 50
Slide covers the agenda of what’s to follow.

## Slide 51
Rp
Rp
Rp
Rp
VDD
VDD
VDD
VDD
1
0
0
0
1
0
0
0
VDD
VDD
VDD
Rn
Rn
Rn
Rn
Rn
Rn
W3
W2
W1
W0
BL3
BL2
BL1
BL0
ROM cell array
Example: 4x4 cell array
Notes: 51
Slide covers the agenda of what’s to follow.

## Slide 52
Rp
Rp
Rp
Rp
VDD
VDD
VDD
VDD
0
1
0
0
0
0
1
0
VDD
VDD
VDD
Rn
Rn
Rn
Rn
Rn
Rn
W3
W2
W1
W0
BL3
BL2
BL1
BL0
ROM cell array
Example: 4x4 cell array
Notes: 52
Slide covers the agenda of what’s to follow.

## Slide 53
Rn
Rn
Rp
Rp
Rp
Rp
VDD
VDD
VDD
VDD
0
0
1
0
0
1
1
0
VDD
VDD
Rn
Rn
Rn
Rn
W3
W2
W1
W0
BL3
BL2
BL1
BL0
ROM cell array
Example: 4x4 cell array
Notes: 53
Slide covers the agenda of what’s to follow.

## Slide 54
Rn
Rn
Rp
Rp
Rp
Rp
VDD
VDD
VDD
VDD
0
0
0
1
1
0
0
1
VDD
VDD
Rn
Rn
Rn
Rn
W3
W2
W1
W0
BL3
BL2
BL1
BL0
ROM cell array
Example: 4x4 cell array
Notes: 54
Slide covers the agenda of what’s to follow.

## Slide 55
Special MOS transistor for
EPROM & EEPROM
p substrate
n+
n+
S
D
G
SiO2
Poly of main Gate
Floating Gate
High Voltage
Programming
Vgsmax (in normal operation mode)
Programmed transistor will be OFF always in normal operation mode
Only non-programmed transistor can be ON/OFF in normal operation mode
This transistor has been programmed, its VT is higher than Vgsmax
WL
ON
OFF
Floating Gate MOS (FGMOS)
p substrate
n+
n+
S
D
G
SiO2
Poly of main Gate
Floating Gate
Notes: 55
Slide covers the agenda of what’s to follow.

## Slide 56
Special MOS transistor for
EPROM & EEPROM
Erase the data in EPROM
p substrate
n+
n+
S
D
G
SiO2
Poly of main Gate
Floating Gate
Apply violet light to the gate to release trapped electrons in the floating gate back to the substrate. This process is used to erase the EPROM before programming new data.
p substrate
n+
n+
S
D
G
SiO2
Erase the data in EEPROM
Floating Gate of FLOTOX MOS, used for EEPROM
Apply high voltage to Drain
Apply high voltage to the Drain of programmed transistor to release trapped electrons in the floating gate. This process is used to erase the EEPROM before programming new data.
Notes: 56
Slide covers the agenda of what’s to follow.

## Slide 57
Part 2
Static Random Access Memory
SRAM
Notes: 57
Slide covers the agenda of what’s to follow.

## Slide 58
SRAM cell array
BL
BLX
WL
SRAM cell
One column
One row
1
0
1
0
Two inverters connected back to back forming a bi-stable circuit, used for storing the data in the cell.
Two transistors used for connecting the cell to BL and BLX for writing/ reading operations. They are called pass-gate transistors and they are ON when the word line (WL) is HIGH
Notes: 58
Slide covers the agenda of what’s to follow.

## Slide 59
0
OFF
OFF
1
0
VDD
GND
1
0
0
1
0
BL
BLX
WL
1
VDD
GND
1
0
0
0
1
BL
BLX
WL
1
0
1
Writing [1] into a cell which currently storing [1]
Writing [0] into a cell which currently storing [1]
SRAM Cell
Writing operation
Notes: 59
Slide covers the agenda of what’s to follow.

## Slide 60
SRAM Cell
Reading operation
0
OFF
OFF
1
0
VDD
GND
1
0
0
BL
BLX
WL
1
GND
CBL
GND
CBLX
+
+
+V
1
1
0
time
time
WL
BL/BLX
Reading time
Due to large BL/BLX capacitance, if we wait until BL or BLX discharges completely to read the data out, reading time is very long.
Sense amplifier is used to reduce reading time  speed up the speed of memory
V
Turn on the Sense Amplifier to reduce reading time
Notes: 60
Slide covers the agenda of what’s to follow.

## Slide 61
SRAM Cell
Reading operation
VDD
GND
1
0
1
BL
BLX
WL
GND
CBL
GND
CBLX
+
+
+V
Vp
Vp-V
RBL
RBLX
GND
SAEN
VDD
SAENX
YA
COLX
V
1
1
0
0
0
1
1
V
GND
CRBL
GND
CRBLX
MEM Core
+
+
Vp
Vp-V
Vp
Vp-V
0
1
Turn on the SA
RBL
RBLX
V
Wrong reading
Notes: 61
Slide covers the agenda of what’s to follow.

## Slide 62
SRAM
WL driver
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
SRAM
Cell
. . . . . . . .
. . . . . . . .
Column 0
Column 1
Column 2
Column n-1
WL0
WL1
WL2
WLm-1
WL Driver
Notes: 62
Slide covers the agenda of what’s to follow.

## Slide 63
SRAM
WL driver
. . . . . . . .
WLx
WL Driver
2
1
3
n
1
2
3
n
time
Due to long WL  high WL capacitance.
If the Driver is not strong enough, the signal at the end of the WL would be not high enough to turn on the cell.
An inverter chain with optimum fan-out number is used to minimize the delay.
The pulse of WL signal must be long enough to read/write the cell at the and of WL completely.
+
+
+
+
Notes: 63
Slide covers the agenda of what’s to follow.

## Slide 64
Part 3
Content Addressable Memory
CAM
Notes: 64
Slide covers the agenda of what’s to follow.

## Slide 65
Content Addressable Memory is a special kind of memory!
Read operation in traditional memory:
  Input is address location of the content that we are interested in it.
  Output is the content of that address.
In CAM it is the reverse:
  Input is associated with something stored in the memory.
  Output is location where the associated content is stored.
Content Addressable Memory (CAM)
Address in
Data out
Search key in
Address out

## Slide 66
CAM can be used as a search engine.
We want to find matching contents in a database or Table.
Example Routing Table
Source: http://pagiamtzis.com/cam/camintro.html
Content Addressable Memory (CAM)

## Slide 67
Content Addressable Memory (CAM)

## Slide 68
Content Addressable Memory (CAM)

## Slide 69
The search-data word is loaded into the search-data register.
All match-lines are pre-charged to high (temporary match state).
Search line drivers broadcast the search word onto the differential search lines.
Each CAM core compares its stored bit against the bit on the corresponding search-lines.
Match-lines that have at least one missing bit, discharge to ground.
Source: K. Pagiamtzis, A. Sheikholeslami, “Content-Addressable Memory (CAM) Circuits and Architectures: A Tutorial and Survey,” IEEE J. of Solid-state circuits. March 2006
Content Addressable Memory (CAM)

## Slide 70
Content Addressable Memory (CAM)
CAM
Binary CAM (BCAM)
Ternary CAM (TCAM)
BCAM can only express ‘0’ or ‘1’
(2 values >> need only 1 memory cell ).
TCAM can express ‘0’, ‘1’, and ‘X’ (don’t care).
(3 value >> need 2 memory cells).

## Slide 71
TCAM bit-cell
MWL
CWL
HL
MWL
CWL
HL
BL
BLX
HBL
HBLX
TCAM cell
TCAM cell
TCAM cell
TCAM cell
One column
One row
Notes: 71
Slide covers the agenda of what’s to follow.

## Slide 72
TCAM bit-cell
VDD
Pre-charge
Encoder
. . . . . . .
. . . . . . .
MLSA
MLSA
One TCAM cell
BL
BLX
MWL
GND
ICBL
ICBLX
IMBL
IMBLX
HBL
HBLX
CWL
HL
Notes: 72
Slide covers the agenda of what’s to follow.

## Slide 73
BL
BLX
MWL
GND
ICBL
ICBLX
IMBL
IMBLX
HBL
HBLX
CWL
HL
1
0
1
TCAM
Writing operation
Writing data to a TCAM bit-cell is similar to that of SRAM
The data is being written into this cell
1
0
VDD
Pre-charge
Encoder
. . . . . . .
. . . . . . .
MLSA
MLSA
Notes: 73
Slide covers the agenda of what’s to follow.

## Slide 74
BL
BLX
MWL
GND
ICBL
ICBLX
IMBL
IMBLX
HBL
HBLX
CWL
HL
0
1
1
0
TCAM
Writing operation
The data is being written into this cell
1
0
VDD
Pre-charge
Encoder
. . . . . . .
. . . . . . .
MLSA
MLSA
Notes: 74
Slide covers the agenda of what’s to follow.

## Slide 75
BL
BLX
MWL
GND
ICBL
ICBLX
IMBL
IMBLX
HBL
HBLX
CWL
HL
0
0
1
0
1
0
MISS
TCAM
Compare operation
VDD
Pre-charge
Encoder
. . . . . .
. . . . . . .
MLSA
MLSA
1. Pre-charge HL
2. Broadcast the search word onto the differential search lines
3. IF miss, HL will discharge to GND
IF match, HL will remain at pre-charge level
4. MLSA detects its ML that has a miss
Notes: 75
Slide covers the agenda of what’s to follow.

## Slide 76
BL
BLX
MWL
GND
ICBL
ICBLX
IMBL
IMBLX
HBL
HBLX
CWL
HL
0
0
1
0
0
1
MATCH
TCAM
Compare operation
VDD
Pre-charge
Encoder
. . . . . . .
. . . . . . .
MLSA
MLSA
1. Pre-charge HL
2. Broadcast the search word onto the differential search lines
3. IF miss, HL will discharge to GND
IF match, HL will remain at pre-charge level
Notes: 76
Slide covers the agenda of what’s to follow.

## Slide 77
BL
BLX
MWL
GND
ICBL
ICBLX
IMBL
IMBLX
HBL
HBLX
CWL
HL
0
0
0
1
1
0
MATCH
TCAM
Compare operation
VDD
Pre-charge
Encoder
. . . . . . .
. . . . . . .
MLSA
MLSA
Notes: 77
Slide covers the agenda of what’s to follow.

## Slide 78
BL
BLX
MWL
GND
ICBL
ICBLX
IMBL
IMBLX
HBL
HBLX
CWL
HL
0
0
0
1
0
1
MISS
TCAM
Compare operation
VDD
Pre-charge
Encoder
. . . . . . .
. . . . . . .
MLSA
MLSA
Notes: 78
Slide covers the agenda of what’s to follow.

## Slide 79
BL
BLX
MWL
GND
ICBL
ICBLX
IMBL
IMBLX
HBL
HBLX
CWL
HL
0
0
0
0
0
1
MATCH ALWAYS
TCAM
Compare operation
VDD
Pre-charge
Encoder
. . . . . . .
. . . . . . .
MLSA
MLSA
Notes: 79
Slide covers the agenda of what’s to follow.

## Slide 80
BL
BLX
MWL
GND
ICBL
ICBLX
IMBL
IMBLX
HBL
HBLX
CWL
HL
0
0
0
0
1
0
TCAM
Compare operation
VDD
Pre-charge
Encoder
. . . . . . .
. . . . . . .
MLSA
MLSA
MATCH ALWAYS
Notes: 80
Slide covers the agenda of what’s to follow.

## Slide 81
BL
BLX
MWL
GND
ICBL
ICBLX
IMBL
IMBLX
HBL
HBLX
CWL
HL
0
0
1
1
1
0
MISS ALWAYS
TCAM
Compare operation
VDD
Pre-charge
Encoder
. . . . . . .
. . . . . . .
MLSA
MLSA
Notes: 81
Slide covers the agenda of what’s to follow.

## Slide 82
BL
BLX
MWL
GND
ICBL
ICBLX
IMBL
IMBLX
HBL
HBLX
CWL
HL
0
0
1
1
0
1
MISS ALWAYS
TCAM
Compare operation
VDD
Pre-charge
Encoder
. . . . . . .
. . . . . . .
MLSA
MLSA
Notes: 82
Slide covers the agenda of what’s to follow.

## Slide 83
TCAM
Compare operation - Summary
Mask-cell
Core-cell
Compare
[0]
[1]
ML
Search bit
[1]
Storing bit [1]
Match
Mask-cell
Core-cell
Compare
[1]
[0]
ML
Search bit
Storing bit [0]
[1]
Miss
Mask-cell
Core-cell
Compare
[0]
[0]
ML
Search bit
Storing bit [X]
Match
[X]
Mask-cell
Core-cell
Compare
[1]
[1]
ML
Search bit
[X]
Miss
We can imagine that a TCAM cell can store bit [0], or bit [1], or bit [X]. The technique is using 2 SRAM cells for those. Each cell must be written independently if they share the same BL/BLX.
Don’t use
In case a TCAM cell stores bit [X], it matchs always with the data bit. This case is used if we don’t want to compare any specific bit in any search word, and the bit [X] can be stored at any location of the Memory cell array.
If we don’t want to compare any specific bit in all search words, bits [X] must be stored in the same column.
Notes: 83
Slide covers the agenda of what’s to follow.

## Slide 84
TCAM
Compare operation - Example
Encoder
Pre-charge
VDD
MLSA
Pre-charge
VDD
MLSA
Pre-charge
VDD
MLSA
Pre-charge
VDD
MLSA
A1
A0
D2
D1
D0
Search word
HBL2
HBL2X
HBL1
HBL1X
HBL0
HBL0X
ML3
ML2
ML1
ML0
Search data register/ driver/ global mask
Address out
TCAM cell array
Notes: 84
Slide covers the agenda of what’s to follow.

## Slide 85
TCAM
Compare operation - Example
Encoder
Pre-charge
VDD
MLSA
Pre-charge
VDD
MLSA
Pre-charge
VDD
MLSA
Pre-charge
VDD
MLSA
A1
A0
D2
D1
D0
Search word
HBL2
HBL2X
HBL1
HBL1X
HBL0
HBL0X
ML3
(11)
ML2
(10)
ML1
(01)
ML0
(00)
Search data register/ driver/ global mask
Address out
0
0
1
0
1
1
1
0
0
1
1
0
0
1
1
0
1
1
0
1
0
1
0
The match-line on which all bits match
remains in the pre-charged-high state
Match-lines that have at least one bit that miss, discharge to GND. High capacitance of ML leads to long discharge time. To speed up the comparison, MLSA is used.
Notes: 85
Slide covers the agenda of what’s to follow.

## Slide 86
TCAM
Compare operation - Example - Global mask
Priority Encoder
Pre-charge
VDD
MLSA
Pre-charge
VDD
MLSA
Pre-charge
VDD
MLSA
Pre-charge
VDD
MLSA
A1
A0
D2
D1
D0
Search word
HBL2
HBL2X
HBL1
HBL1X
HBL0
HBL0X
ML3
(11)
ML2
(10)
ML1
(01)
ML0
(00)
Search data register/ driver/ global mask
Address out
0
0
1
0
1
1
1
0
0
1
1
0
0
1
1
0
1
1
1
1
0
1
0
There could be more than one match-line on which all bits match. In this case, the encoder must be priority encoder type instead of normal encoder. Normally, lower address, higher priority.
Notes: 86
Slide covers the agenda of what’s to follow.

## Slide 87
Thank You !